## Slide 1: ECE 260C, Spring 2025 Placement
Andrew B. Kahng
Thanks to: Andrew Kennings, Mingyu Woo, SangGi Do, Nima Darav
Kahng ECE 260C SP25

## Slide 2: Physical Design Flow Pictures (old ECE 260B slide)
Floorplanning
Powerplanning
Placement
Routing

## Slide 3: Global Placement
Kahng ECE 260C SP25
Notes: THIS placement. There are around 300 thousand standard cells in this picture. The global placement gets things roughly into the right places.

## Slide 4: GPL
Kahng ECE 260C SP25

## Slide 5: RePlAce: Advancing Solution Quality and Routability Validation in Global Placement
Chung-Kuan Cheng, Andrew B. Kahng, Ilgweon Kang and Lutong Wang
(based on slides from Ilgweon Kang’s Ph.D. defense)
paper
Kahng ECE 260C SP25

## Slide 6: Placement Overview
Placement
  Determines the locations of standard cells and/or logic elements while addressing optimization objectives
  Highly important physical design step in integrated circuit (IC) design flow
    Directly impacts on timing closure, die utilization, routability, design turnaround time (TAT)  operating frequency, yield, power consumption, cost
Placement instances
  Hypergraph G = (V, E)
    V:= a set of vertices, i.e., standard cells and macros
    E:= a set of hyperedges, i.e., nets
Placement solution v = (x, y), X- and Y-coordinates of all placeable vertices
  legal solution?
    Every instance should be settled in the placement region.
    Every standard cell should be spaced within predefined rows.
    No overlap is allowed between instances including both standard cells and macros.
A. B. Kahng, J. Lienig, I. L. Markov and J. Hu, VLSI Physical Design: From Graph Partitioning to Timing Closure, Springer, 2011
Kahng ECE 260C SP25

## Slide 7: Problem Formulation
Placement Objective Function f(v)
ePlace: Electrostatics-based global-smooth density function
Cell Instance
Cell Area (Ai)
Placement Instance
Even Density Distr.
Cell Coordinate & Dim.
Electric Particles
Charge Quantity (qi)
Electrostatic System
Min. Potential Energy
Charge Coordinate & Dim.
[13] J. Lu, “Analytic VLSI Placement Using Electrostatic Analogy”, Ph.D. Dissertation, UC San Diego, CA, 2014.
Kahng ECE 260C SP25

## Slide 8: ePlace: In Each Iteration
charge density distr.
electric potential distr.
cell & macro distr.
electric field distr.
ρ(x, y)
sol. v
ψ(x, y)
E(x, y)
J. Lu, “Analytic VLSI Placement Using Electrostatic Analogy”, Ph.D. Dissertation, UC San Diego, CA, 2014.
Kahng ECE 260C SP25

## Slide 9: RePlAce
Unified placement engine which solves multiple classes of academic benchmarks (mixed-size, fixed-macros, routability-driven, etc.
Local Lagrange multiplier
  Enables local smoothing w/awareness of local over-demanded bins
Meta parameter tuning
  Adjust step size of numerical method
Routability optimization
  Simple but effective metal layer-aware superlinear cell inflation
Differences from the previous ePlace 2.0
  Routability optimization techniques
  Code optimizations for ~4X speedups
  Various improvements to placement mechanisms
    E.g., macro legalization using annealing; amount of rollback after fixing macro; handling of overflows; bin size determination and local smoothing; …
Kahng ECE 260C SP25

## Slide 10: RePlAce: Constraint-Driven Placement
Local Lagrangian multiplier νj
  Local-Density Penalty Factor for each bin bj
  BinDemandj = total cell area in bin bj
  BinCapacityj = area of bin bj
  BinDemandj - BinCapacityj = of bin bj.
[ePlace]
[RePlAce with Constraint-Driven]
Kahng ECE 260C SP25

## Slide 11: RePlAce: Constraint-Driven Placement
  Local-Density Cost Coefficient for each cell
  The previously defined νj was insufficient for local smoothing
  Cellfrom high-overflow bin losts a large amount of local-oriented repulsive force
  Δi helps to memorizes previously obtained local force.
Local smoothing without local-density cost coefficient
Local smoothing with local-density cost coefficient
Kahng ECE 260C SP25

## Slide 12: RePlAce: Constraint-Driven Placement
Global placement animation with local Lagrangian multiplier
NEWBLUE1, [RePlAce with local Lagrangian multiplier, i.e., constraint-driven placement]
HPWL = 5.60E+7, #Iter = 762 (623+139), runtime = 9.9 min, target density = 100%
Comparison: ePlace 2.0 with local Lagrangian multiplier
HPWL = 5.71E+7, #Iter = 1078 (609 + 469), runtime = 42 min, target density = 100%
Kahng ECE 260C SP25

## Slide 13: RePlAce: Dynamic Step Size
General Idea of Dynamic Step Size
(a)
(b)
(c)
Kahng ECE 260C SP25

## Slide 14: RePlAce: Improved Dynamic Step Size
  Methodology to capture “transition points” on HPWL curve.
▲ HPWL curve of ADAPTEC1 (MMS) from the trial placement procedure and the estimated transition points (TPs)
▲ Flowchart of trial placement procedure. The red rectangle indicates nonlinear optimization using Nesterov’s method. The actual placement procedure follows this tGP procedure.
Kahng ECE 260C SP25

## Slide 15: RePlAce: Improved Dynamic Step Size
Solution quality in terms of the final HPWL
  ePlace vs. RePlAce-ds (ADAPTEC1)
    RePlAce-ds achieves a dominating runtime and solution quality (red square)
    Below [0.95, 1.003], e.g., [0.95, 1.002], [0.95, 1.001], etc., runs did not converge
Kahng ECE 260C SP25

## Slide 16: RePlAce: Routability-Driven Placement
Simple but effective routability optimization
  A layer-aware cell inflation technique
  Integrate the official global router NCTU-GR [17] of the DAC-2012 [18] and ICCAD-2012 [19] benchmark suites for congestion estimation.
  Superlinear cell inflation technique to mitigate global routing congestion during global placement.
  We further include a post-placement optimization by [20]
    Following the strategy of recent leading works [21] [22]
[17] NCTU-GR, http://people.cs.nctu.edu.tw/˜whliu/NCTU-GR.htm
[18] N. Viswanathan, C. J. Alpert, C. N. Sze, Z. Li and Y. Wei, “The DAC 2012 Routability-driven Placement Contest and Benchmark Suite”, Proc. DAC, 2012, pp. 774-782.
[19] N. Viswanathan, C. J. Alpert, C. N. Sze, Z. Li and Y. Wei, “ICCAD-2012 CAD Contest in Design Hierarchy Aware Routability-Driven Placement and Benchmark Suite”, Proc. ICCAD, 2012, pp. 345-348.
[20] W.-H. Liu, C.-K. Koh and Y.-L. Li, “Optimization of Placement Solutions for Routability”, Proc. DAC, 2013, pp. 1-9.
[21] X. He, T. Huang, L. Xiao, H. Tian and E. F. Y. Young, “Ripple: A Robust and Effective Routability-Driven Placer”, IEEE Trans. on CAD 32(10) (2013), pp. 1546-1556.
[22] X. He, Y. Wang, Y. Guo and E. F. Y. Young, “Ripple 2.0: Improved Movement of Cells in Routability-Driven Placement”, ACM Trans. on DAES 22(1) (2016), pp. 10:1-10:26.
Kahng ECE 260C SP25

## Slide 17: RePlAce: Routability-Driven Placement
Metal layer-aware superlinear cell inflation
  = one of the four edges of a given global routing tile
  = a specific metal layer
  = 2.33 (empirically determined)
  Considers the total available whitespace
    Starting from 90% die utilization,
    We limit ‘the maximum cell-inflated area’ ≤ 10%
    If exceed, then perform ‘inflation ratio adjustment’
      Divides the inflation ratio for each tile by the inflation ratio of the least-congested tile that has a ratio greater than one
Routing demand calculation: the upper-left tile has a horizontal routing demand of = 19
▲
Blockage calculation. For the vertical edge on the right,
. Note the union of blocked capacity for the upper two blockages.
▲
Kahng ECE 260C SP25

## Slide 18: RePlAce: Routability-Driven Placement
IEEE Trans. on CAD paper: routability optimization flow
Uses the detailed placer from NTUplace3
T.-C. Chen, Z.-W. Jiang, T.-C. Hsu, H.-C. Chen and Y.-W. Chang, “NTUplace3: An Analytical Placer for Large-Scale Mixed-Size Designs with Preplaced Blocks and Density Constraints”, IEEE Trans. on CAD 27(7) (2008), pp. 1228-1240.
Kahng ECE 260C SP25

## Slide 19: RePlAce: Routability-Driven Placement
Global routing overflow (SUPERBLUE12) during routability-driven global placement procedure
Kahng ECE 260C SP25

## Slide 20: RePlAce: Routability-Driven Placement
Global placement animation with our routability optimization
  Keeps the inflated cell size by the end of global placement
  Red-cell zone is keep growing along with the routability optimization
  SUPERBLUE18 (ICCAD-2012)
  The initial RC value = 135.23
  The final RC value = 102.10
  SUPERBLUE12 (DAC-2012)
  The initial RC value = 211.73
  The final RC value = 102.43
Kahng ECE 260C SP25

## Slide 21: RePlAce (2019) Summary
Advancing solution quality and routability validation in GPL
  Local density function
    Local smoothing comprehending local over-demanded bins
  Improved dynamic step size adaptation
  Routability optimization
    Simple but effective metal layer-aware superlinear cell inflation technique
Superior solution quality for range of problem types
  Standard cell placement: average HPWL reduction of 2.00% over best previous ISPD benchmark results
  Mixed-size placement: average HPWL reduction of 2.73% over the best previous MMS benchmark results
  Routability-driven placement: average 8.50% to 9.59% scaled HPWL reduction over previous leading academic placers for DAC-2012 and ICCAD-2012 benchmark suites
Notes
Formulation is here (calculate demand / capacity) and here
Dynamic step size updating is here
Entry point for routability-driven is here
Calculation of cell inflation for routability-driven placement is here and here
Kahng ECE 260C SP25

## Slide 22: Global Placement Zoom-In
Kahng ECE 260C SP25
Notes: And, if we zoom in to the global placement, you can see that cells are definitely not placed into nice rows. What’s more, even at this stage, it’s already pretty obvious where there are electrical or timing problems in this layout that we’re creating. For instance, a high-fanout net with 80 pins is going to have terrible delays and transition times at its sinks, unless we add some buffers to break up that high fanout. Or, a long net that delivers a signal from driver to a far-away receiver will need buffering as well. So, OpenROAD performs OPTIMIZATION at this juncture, including inserting buffers or upsizing weak drivers.

## Slide 23: (Legalized) Detailed Placement Zoom-In
Kahng ECE 260C SP25
Notes: After this, the standard-cells are LEGALIZED into rows, and users have the option to call further DETAILED PLACEMENT optimizations of wirelength or routability while maintaining the legal, row-based nature of the placement.

## Slide 24: Region constraints
Cells assigned to a region have to be placed inside the boundary of the region.
mgc_superblue16_a
Zoomed area containing a region constraint
Thanks: Nima Darav, AMD
Notes: As the size of transistors shrinks, more complicated constraints are imposed.
Some important modern technology constraints considered in this proposal are:
Region constraints which assign some cells to specific region. Cells assigned to a region have to be placed inside the boundary of the region.

## Slide 25: Fence region constraints
Cells assigned to a fence region have to be placed inside the boundary of the region while other cells need to be placed outside.
mgc_superblue16_a
Zoomed area
Thanks: Nima Darav, AMD
Notes: Cells assigned to a fence region have to be placed inside the boundary of the region while other cells have to be placed outside of the boundary.
Violating fence region constraints makes the placement unacceptable and these constraints are generally considered as hard constraints.

## Slide 26: Edge spacing constraints
Two cells are too close to each other
Prone to pin access and short problems
Thanks: Nima Darav, AMD
Notes: Edge spacing rules are a minimum space between two or more objects. In this example, the shown two cells are too close to each other, therefore, the pins in pink are prone to pin access or short problems

## Slide 27: DPL
Kahng ECE 260C SP25

## Slide 28: Legalization and detailed placement
Global placement must be legalized
  Cell locations typically do not align with power rails
  Small cell overlaps due to incremental changes, such as cell resizing or buffer insertion
Legalization seeks to find legal, non-overlapping placements for all placeable modules
Legalization can be improved by detailed placement techniques, such as
  Swapping neighboring cells to reduce wirelength
  Sliding cells to unused space
Software implementations of legalization and detailed placement are often bundled (dpl)
Thanks: Sang-Gi Do, Samsung

## Slide 29: Mixed-height standard cell legalization
Legalization: seek legal placement + remove overlaps
Mixed-height standard cells: standard cells that span different row heights  single/double/triple/quadruple
Mixed-height standard cell legalization is challenging
  Potential overlaps in vertical (+ horizontal) directions
  Horizontal movement of a multi-height cell disrupts placement across all rows it overlaps
Presence of fence regions aggravate the problem
Thanks: Sang-Gi Do, Samsung

## Slide 30: An example of power rails violation
Red bars: power (VDD); blue bars: ground (VSS)
A1, A2: single height standard cells; B1, B2: double height standard cells; C1, C2: triple height standard cells
B2 and B3 violate power rails alignment
Thanks: Sang-Gi Do, Samsung

## Slide 31: Overall framework in dpl
Fence region-aware (FRA) BFS algorithm (paper)
Cell arrangement
Local cell shifting
Corner weight move
Cell move
Cell swap
Global placement result
Pre-legalization
Multi-height legalization
Refinement
Greedy refinement
Find nearest available position
Shift peripheral cells
Move cells towards corner of fence region
Legalize cells that violate fence regions
Multi-height legalization: fence region-aware BFS
Thanks: Sang-Gi Do, Samsung

## Slide 32: Pre-legalization – an example
Grey cells outside fence region are pushed into the fence region
Fence region
Before pre-legalization
After pre-legalization
Thanks: Sang-Gi Do, Samsung

## Slide 33: Corner weight move – an example
Push standard cells towards the corners of the fence region
Before corner weight moves
After corner weight moves
Thanks: Sang-Gi Do, Samsung

## Slide 34: Local shifting – an example
Set a region around violating cell + rearrange peripheral cells to resolve violation
Define region (clip) around violating cell
Disallowed cells
Allowed cells
Re-arrange peripheral cells

## Slide 35: Cell swaps – an example
Benchmark : des_perf_b_md2. Cell count : 112644. Max cell row : 4 Fence Utilization : 96.2%
Before swap
After swap
Thanks: Sang-Gi Do, Samsung

## Slide 36: DPO
Kahng ECE 260C SP25

## Slide 37: DPO in a nutshell (1/2)
DPO runs a detailed placement “script” that can perform a sequence of different optimization algorithms (see Optdp.cpp).
Implemented algorithms (variations of what’s been described in literature as there are many incarnations of the different algorithms): Maximum independent set matching [1], Optimal reordering [2], Median improvement (global and vertical swapping) [3], greedy improvement [4]
Sample script string:
dtParams.script_ = “mis –p 10 –t 0.005’ gs –p 10 –t 0.005 ; vs –p 10 –t 0.005; ro –p 10 –t 0.005; default –p 5 –f 20 –gen rng –obj hpwl –cost (hpwl)”
Dpo::Detailed dt(dtParams);
dt.improve(mgr);
algorithm to run (e.g., gs = global swap, ro = optimal reordering, etc.)
algorithm-specific parameters
runs the script
Thanks: Andrew Kennings, Altera
Kahng ECE 260C SP25

## Slide 38: DPO in a nutshell (2/2)
Most algorithms can optimize hpwl or displacement (other objectives such as timing, congestion, etc.) are not well accounted for which is a “consequence” of the algorithm.
The greedy algorithm is actually very flexible; it uses the idea of “move generators” and “cost objects” that can propose any set of cell movements (cells assigned to new locations) which are then evaluated by the “cost objects” to form a cost function.
  Proposed moves are accepted or rejected based on cost and move generators and cost objects track the current state of the placement (for incremental computation).
  Need to be careful to support the required object pieces to add something; e.g., routines need accept() and reject() methods.
DPO is largely not great with multi-height cells
  E.g., greedy algorithm can only do simple swaps and moves and is not good at “shifting other cells out of the way”.
Thanks: Andrew Kennings, Altera
Kahng ECE 260C SP25

## Slide 39: Some References
K. Doll, F. M. Johannes, and K. J. Antreich. “Iterative placement improvement by network flow methods”, IEEE Trans. Computer-Aided Design of Integrated Circuits and Systems, 13(10):1189-1200, 1994
A. E. Caldwell, A. B. Kahng and I. L. Markov, “Optimal partitioners and end-case placers for standard-cell layout”, Proc. ACM Intl. Symp. on Physical Design, April 1999, pp. 90-96.
Min Pan, Natarajan Viswanathan and Chris Chu, “An efficient and effective detailed placement algorithm”, IEEE/ACM International Conference on Computer-Aided Design, pages 48-55, 2005.
Andrew A. Kennings, Nima Karimpour Darav, Laleh Behjat “Detailed placement accounting for technology constraints VLSI-SoC 2014:1-6
Kahng ECE 260C SP25

## Slide 40: BACKUP
Kahng ECE 260C SP25